## Slide 1: Simplification of numeric variables for PLC model checking
Ignacio D. Lopez-Miguel (CERN)
20/11/2021
Dr. Jean-Charles Tournier (CERN)
Dr. Borja Fernandez Adiego (CERN)
Dr. Juan A. Rodríguez-Aguilar (IIIA-CSIC)
Dr. Enrique Blanco Viñuela (CERN)

## Slide 2: Context – European Organization for Nuclear Research (CERN)
  Basic science: fundamental structure of the particles.
  Technology: world's largest and most complex scientific instruments.

## Slide 3: Context – Safety-critical industrial applications
Cryogenics
Access control and Protection systems
These systems use PLCs (Programmable Logic Controllers) as a control device
An error could cause a disaster
Guarantee safety: Test every single possibility

## Slide 4: Context – Model Checking for PLCs
4 Integer (16-bit) input variables  216⋅4 ≈ 1.8⋅1019 combinations
Input1
Input2
Input3
Input4
Output1
Output2
PLC program
Functionality requirement
If Input1 is False, then Output2 is False
Safety requirement
If Output1 is False, then Output2 is True
Solution: Model checking
Problem: state-space explosion
Goal: Simplification of numeric variables
Sensors
Actuators

## Slide 5: Model Checking for PLCs – Standard workflow
Model Checker
Solver

Property OK

Property failed
Counterexample
Real System
(software)
Specifications
Temporal Logic
Control-flow automaton (CFA)
Formal model
Formal requirement
PLCverif
Hides the complexity of using formal methods
20/09/2021
init
l1
l2
l3
in>10
out1  False
out1  True
in≤10
out2  True
out2  False
l0
in  IntNonDet()

## Slide 6: Model checking challenges – Variable simplification
Formal specification
Requirement formalization
Counterexample analysis
State-space explosion
  Several variables
  A lot of interaction among variables
  Big data types
    Integers
    Reals
    Words

## Slide 7: Variable simplification – State of the art
Counterexample-guided abstraction refinement (CEGAR)
Predicate abstraction
Satisfiability Modulo Theories (SMT)
Manual boundary setting
Deficiencies
  Refinement needed
  Specific to the model checker
  Manual
  One single counterexample given
  Not widely used for PLC programs

## Slide 8: Variable simplification – Contribution
CFA structural patterns analysis
Variable discretization
CFA transformation
Family of transformations
Agnostic to the model checker
No refinement needed
Richer counterexamples
Experimental results

## Slide 9: Variable simplification – Conditional pattern example
X has 5 possible values
-50
0
20
50
x
0
1
2
3
4
x
FUNCTION_BLOCK example
VAR_INPUT
x : INT;
END_VAR
VAR_OUTPUT
y : INT;
END_VAR
BEGIN
IF x>0 THEN
IF x>50 THEN
y := 3;
ELSE
y := 2;
END_IF;
ELSE
IF x<-50 THEN
y := 0;
ELSE
y := 1;
END_IF;
END_IF;
//#ASSERT (y=0 AND x>20);
END_FUNCTION_BLOCK
From 65536 possible values to 5
PLC program
Original CFA
Transformation
Transformed CFA
x has 216=65536 possible values
Init
Error
Init
Error

## Slide 10: Variable simplification – Assignment pattern example
FUNCTION_BLOCK example2
VAR_IN_OUT
x : INT;
END_VAR
VAR_OUTPUT
y : INT;
END_VAR
BEGIN
IF x>0 THEN
x := x-1;
IF x>50 THEN
y := 3;
ELSE
y := 2;
END_IF;
ELSE
x := x+1;
IF x<-50 THEN
y := 0;
ELSE
y := 1;
END_IF;
END_IF;
//#ASSERT (y=0 AND x>20);
END_FUNCTION_BLOCK
PLC program
Original CFA
Node duplication
Assignment removal
Init
Error
Init
Error
-51
0
19
51
x
0
1
2
3
4
x
21
5
Init
Error
1
Conditional pattern
From 65536 possible values to 6

## Slide 11: Variable simplification – Experiments
Theta
Three state-of-the-art model checkers
Different CFAs
Several executions to have significant results
BDD
SMT, CEGAR
SAT

## Slide 12: Conclusions – Results
Theta
Speed-ups of two orders of magnitude.
Terminating now programs that timed out.
-50
0
20
50
x
0
1
2
3
4
x
Agnostic to the model checker.
init
l1
l2
l3
in>10
out1  False
out1  True
in≤10
out2  True
out2  False
l0
in  IntNonDet ()
Richer counterexamples.
Speed-ups of up to 17x when the property is satisfied
Small speed-ups
Worse results when the CFA includes complex patterns

## Slide 13: Conclusions – Future work
Implement in PLCverif
Automate the transformation
Estimate the computational cost
More efficient discretization encoding
Other
Extend it to other programming languages
Study it for unbounded loops
Include this technique in other fields:
  Formal verification of neural networks
  Safe reinforcement learning

## Slide 14
Thank you

## Slide 15: Index
Context
  CERN
  Safety-critical industrial applications
Model checking for PLCs
  Motivation
  Standard workflow
Variable transformation
  Model checking challenges
  State of the art
  Contribution
  Conditional pattern example
  Experiments
Conclusions
  Results
  Future work
  Remark
Appendix

## Slide 16: Model Checking for PLCs - PLCverif
If Out1 is FALSE
then Out2 is TRUE
AG (!Out1 → Out2)
Formalized requirements
Control Flow Automaton

Property OK
Theta
FUNCTION_BLOCK test
VAR_INPUT
in : INT;
END_VAR
VAR_OUTPUT
out1 : BOOL;
out2 : BOOL;
END_VAR
BEGIN
IF in>10 THEN
out1 := False;
out2 := True;
ELSE
out1 := True;
out2 := False;
END_IF;
END_FUNCTION_BLOCK
init
l1
l2
l3
in>10
out1  False
out1  True
in≤10
Non-deterministic input variables
out2  True
out2  False
Requirements
l0
in  IntNonDeterministic()

Property failed
Trace leading to the violation
PLC program
Intermediate Model
Model checker


Formal model
Formal requirement

## Slide 17: Model checking – Example (SAT-based)
x = BoolNonDeterministic()
if x=True then
y := False
else
y := True
Assert: y=True
x
y  False
y  True
¬x
(x AND ¬y AND ¬y) OR (¬x AND y AND ¬y)
CNF
y
¬y
(¬y) AND (x)
(¬y) AND (x)
2 variables (x, y)
2 clauses (¬y, x)
Counterexample: x=True, y=False
(¬y) AND (x)
1. Program graph
2. Satisfiable (SAT) formula
3. Check satisfiability (DPLL)
1. Make True the first clause.
- Set y=False
2. Make True the second clause.
- Set x=True
If not possible, go to step 1 and choose another variable.
If not possible, formula unsatisfiable.
3. All clauses are True
Conjunctive Normal Form

## Slide 18: Model checking – Example (SMT-based)
(x>10 AND ¬y AND ¬(¬(x<0) OR y)) OR (x≤10 AND y AND ¬(¬(x<0) OR y))
(p AND ¬y AND ¬(¬q OR y)) OR (¬p AND y AND ¬(¬q OR y))
Theory-solver
Find a value for x that makes p=True and q=True
Find another candidate solution adding the constraint:
Invalid counterexample
1. Program graph
2. SMT (Satisfiability Modulo Theories) formula
CNF
3. Check satisfiability
x>10
y  False
x≤10
¬(x<0) OR y
¬(¬(x<0) OR y)
p:= x>10
q:= x<0
y  True
x = IntNonDeterministic()
if x>10 then
y := False
else
y := True
Assert: x<0  y=True
DPLL
Bool encoding of clauses
Theta
SAT formula
(¬y) AND (q) AND (p OR y) AND (¬p OR ¬y)
(¬(x<0) OR y)
3 variables
4 clauses
Property satisfied
¬(p AND q AND ¬y)
(¬y) AND (q) AND (p OR y) AND
(¬p OR ¬y) AND
¬(p AND q AND ¬y)
No solution found
Not possible

## Slide 19: Model checking – Example (BDD-based)
x = BoolNonDeterministic()
if x=True then
y := False
else
y := True
Assert: y=True
end=False
x=False
y=False
end=True
x=True
y=False
end=True
x=False
y=True
(((¬end AND ¬x AND ¬y) AND (end’ AND x’ AND ¬y’))
OR ((¬end AND ¬x AND ¬y) AND (end’ AND ¬x’ AND y’)))
AND (end’ AND ¬y’)
False
True
end
x
y
end'
x'
y’
1. Transition system
2. Formula
3. BDD
Binary Decision Diagram